## Slide 1
UNIVERSAL SERIAL BUS

## Slide 2: GROUP MEMBERS :
TOPIC :
Universal Serial Bus (USB)
NAME: Sushant Kumar
ROLL NO. : B43
SECTION : K23SA
REG. NO. : 12311087
NAME: Arjun Kumar
ROLL NO. : B72
SECTION : K23SA
REG. NO. : 12313473
WELCOME

## Slide 3: CONTENT
Introduction of USB
Evolution of USB
Types of USB Ports & their Common uses
Versions of USB
Color Coding of USB
How USB works & Data transfer rate
USB in computing
USB In Mobile Devices
USB in Peripheral Devices
Advantages of USB
USB Security
USB in everyday life
Conclusion
Questions

## Slide 4: Introduction of USB
What is USB ?
USB stands for Universal Serial Bus.
Allow users to connect a wide variety of peripheral to a computer.
It is used to transfer data from one device to another.
Following are the examples of USB devices:
  Mouse
  Keyboard
  Printer
  Scanner
  Webcams
  Microphones
  Storage devices like pendrives

## Slide 5: Evolution of USB
Ajay V. Bhatt is an Indian-born American computer architect who defined and developed Universal Serial Bus in 1995.
Led a team of 7 Companies to develop USB standard
Ajay V. Bhatt

## Slide 6: Versions of USB
USB TYPE | SPEED TITLE | MAX. BANDWIDTH | REALEASE DATE
USB 1.0 | Low Speed | 1.5 Mbps | January, 1996
USB 1.1 | Full Speed | 12 Mbps | August, 1998
USB 2.0 | High Speed | 480 Mbps | April, 2000
USB 3.0 | Super Speed | 5 Gbps | November, 2008
USB 3.1 | Super Speed + | 10 Gbps | July, 2013
USB 3.2 | SS20 | 20 Gbps | August, 2017
USB 4 | SS40 | 40 Gbps | 2019
USB 4 version 2 | SS80 | 8 0 Gbps | 2022
SS Represents “ Super Speed ”

## Slide 7: Types of USB Cables
USB TYPE | NUMBER OF PINS | VERSION SUPORTED | MAXIMUM SPEEDS | USED IN
Type A | 4 | 2.0, 3.0, 3.1, 3.2 | 480 Mbps, 5 Gbps, 10 Gbps | Computers, tablets, television sets, flash drives, keyboards
Type B | 4 | 2.0, 3.0, 3.1 | 480 Mbps, 5 Gbps | Printers, Scanners
Type C | 24 | 2.0, 3.0, 3.1, 3.2 | 480 Mbps, 5 Gbps, 10 Gbps | Smartphones, headphones
Mini A&B | 5 | 2.0 | 480 Mbps | Digital camera, computer peripherals
Micro A&B | 5 | 2.0 | 480 Mbps | Smartphones, computer peripherals, video game controllers
Lightening Cables | 8 | 3.0 | 480 Mbps, 5 Gbps | Apple’s devices

## Slide 8: Types of USB Cables & Their Uses
Type A
Type B
Type C
Number of Pins : 4
Versions Supported : 2.0, 3.0, 3.1, 3.2
Maximum Speed : 480 Mbps, 5 Gbps, 10 Gbps
Used in : Computers, tablets, television sets, flash drives, keyboards
Number of Pins : 4
Versions Supported : 2.0, 3.0, 3.1
Maximum Speed : 480 Mbps, 5 Gbps
Used in : Printers and Scanners
Number of Pins : 24
Versions Supported : 2.0, 3.0, 3.1, 3.2
Maximum Speed : 480 Mbps, 5 Gbps, 10 Gbps
Used in : Smartphones, Headphones

## Slide 9: Types of USB Cables & Their Uses
Mini A&B
Micro A&B
Lightening Cables
Number of Pins : 5
Versions Supported : 2.0
Maximum Speed : 480 Mbps
Used in : Digital camera, computer peripherals
Number of Pins : 5
Versions Supported : 2.0
Maximum Speed : 480 Mbps
Used in : Smartphones, computer peripherals, video game controllers
Number of Pins : 8
Versions Supported : 3.0
Maximum Speed : 480 Mbps, 5 Gbps
Used in : Apple’s devices

## Slide 10: Overview of Ports in devices

## Slide 11: Color Coding Of USB Ports
USB 1.0
USB 2.0
USB 3.0
USB 3.1
USB 3.2
Provides Charging In Sleep Mode

## Slide 12: How USB Works ?
Key Features:
  Hosts
  Peripheral devices
  Hubs
USB is controlled by hosts.
In USB we consider 7-bit addressing.

## Slide 13
HOST
HUB

## Slide 14: How does USB work ?